## Slide 1: Digital Electronics Lab

## Slide 2: Summary
Exp 1 – Use of counter and 7 segment displays to display numbers
Exp 2 - Use of combinational logic to display a mapping on 7 segment display
Exp 3 – Use of decoder to simplify this mapping
Exp 4 – Display of such two mapping using nibble multiplexers

## Slide 3: Summary
Exp 5 – Use of 4-bit adder circuit and XOR gates to implement addition and subtraction of 4-bit integers
Exp 6 – Use of 4-bit adder circuit to add two 4-bit integers using only one ASCII keyboard and thus storing one of them in a flipflop
Exp 7 – Writing and Reading from RAM
Exp 8 – Extension of Exp 7 with multiple displays (one display is active at any moment)

## Slide 4: Summary
Exp 5 – Use of 4-bit adder circuit and XOR gates to implement addition and subtraction of 4-bit integers
Exp 6 – Use of 4-bit adder circuit to add two 4-bit integers using only one ASCII keyboard and thus storing one of them in a flipflop
Exp 7 – Writing and Reading from RAM
Exp 8 – Extension of Exp 7 with multiple displays (one display is active at any moment)

## Slide 5: Summary
Exp 9 – Implementing 4x4 bit binary adder using registers and down counters
Exp 10 – Implementing 4x4 bit serial parallel multiplier
Exp 11 – Implementing 8-bit binary to BCD converter

## Slide 6: Exp 1 – Counter on 7 segment display
IC 7490 – Convert a counter to its binary form (see exp to initialize the connections)
IC 7447 – Convert a modulo 10 binary number to equivalent representation to be used in 7 segment display
Counters (instruments->digital->pulsar) – Provides clock

## Slide 7: Exp 2 – Display a mapping for each clock
Modulo 8 counter is designed and each instance is mapped to some number using combinational logic.
Old ICs used: 7-segment display (exp 1) and IC 7447 (exp 1)
New IC:
  IC 7493 – Same as IC 7490 (exp 1) but must be preferred over

## Slide 8: Exp 3 – Exp 2 + Decoder
The previous experiment is performed with a decoder
Old ICs used
  7447 (exp 1)
  7493 (exp 2)
New IC used
  74138 – (3-to-8) decoder with active low outputs
    Used in this experiment because it is to design logic when decoder is used

## Slide 9: Exp 4 – Exp3 + Nibble MUX
Experiment is just a re-iteration of experiment 3, however two roll number are to be displayed as per the select line
Old IC used
  7447 (exp 1)
  7493 (exp 2)
  74138 (exp 3)
New IC used
  74157 is a nibble multiplexer that has two 4-bit inputs A and B, and the output O=A is S=0 and O=B if S=1

## Slide 10: Exp 5 – Adding and Subtracting two 4-bit number as per select
Use of 4-bit adder and XOR gate to implement the addition and subtraction as per the select input. It is given that result will be bounded to be displayed on 2 (7 segment) displays. Two (4 bit adder units) are required: one to perform the addition and subtraction, other to add (6) to represent number > 9
Old IC used:
  7447 (exp 1)
New IC used
  7483 – 4-bit adder circuit

## Slide 11: Exp 6 – Addition of 4-bit integers using only one ASCII keyboard and thus storing the previous one
In this experiment, a 4-bit addition was to be carried out. However, there was only one source of input, a ASCII keyboard. Now as we need to operands, one of them is stored in flipflop.
Old IC: 7483 (exp 5)
New IC:
  ASCII keyboard (Switches->Digital): A delay is needed in path from Strobe of ASCII keyboard to CP of flip-flop (reason discusses in manual)
  74273 – 8-bit +ve edge triggered D FF for storage

## Slide 12: Exp 7 – Writing and Reading from RAM
Inputs are written at different memory location of RAM, and can be accessed by that address
The report is self-explanatory (it has 4 controls so read the function of each)
Old IC used
  7447 (exp 1), 7493 (exp 2), counter (exp 1), ASCII (exp 6)
New IC used
  74173 – System bus used for enabling or disabling the incoming inputs (enable while writing, disabled while reading)
  RAM1k (Digital by Function->RAM->RAM1k) – used as memory

## Slide 13: Exp 8 – Exp 7 + multiple displays
Exp 7 is repeated however instead of displaying the stored value on a single display, multiple displays are used. At a time, only one display is used for display. Requires controls.
Circuit is same as that of Exp 7
Only one modification, common cathode are used instead of common anode, and 74138 (3-to-8 decoder) is used to channel which of the display should be active.

## Slide 14: Exp 9 – (4 X 4) bit multiplier
In this experiment, a 4x4 bit multiplier is implemented using registers and down-counters
Reading the report will be enough as the circuitry is quite complex

## Slide 15: Exp 10 – 4x4 bit serial parallel multiplier
See the report for circuitry and details

## Slide 16: Exp 11 – 8 bit binary to BCD converter
See the report for circuitry and details.